## Slide 1
Alaska Department of Transportation & Public Facilities
Updates to the Integrated Vegetation Management Plan
Renée Goentzel
July 21, 2015

## Slide 2: IVMP use procedures established
The focus at DOT&PF has shifted from the content of the IVMP itself to how the IVMP should be implemented. Procedures for both external agency and internal DOT&PF use of the IVMP have now been established beyond the basic monitoring, notification, record keeping, and reporting requirements stated in the IVMP. A series of steps have been developed which include instructions.

## Slide 3: IVMP use procedures for federal and state agencies
Steps:
1. Identify area(s) in need of treatment
2. Choose the appropriate vegetation management tool
3. Make a detailed plan
4. Communicate with DOT&PF M&O environmental staff
5. Start the pre-application checklist
6. Contact the DOT&PF Right-of-Way (ROW) section to apply for a permit
7. Notify the public and ADEC
8. Submit the completed pre-application checklist with required paperwork
9. Implement plan once approved, documenting work as it performed
10. Complete and submit the post-application checklist
11. Required follow up
12. Recordkeeping

## Slide 4: Step 1: Identify area(s) in need of treatment
Identify area(s) in need of treatment and determine whether vegetation within the area is a safety concern or a noxious or invasive weed infestation. If vegetation control is needed to address noxious or invasive weeds, prioritize areas and actions by species, invasiveness ranking, and control versus potential elimination of the species. Other questions to consider include:
Does the invasive/noxious weed have the potential to cause significant ecological harm or harm to human health or the economy?
Does the size and number of infestations increase the cost and probability of success to the point that control is unlikely?
Will removing the invasive/noxious weed allow native plants to flourish, or will a nearby infestation of the same or another invasive likely dominate instead?
Is the goal containment, suppression, or eradication?

## Slide 5: Step 2: Choose the appropriate vegetation management tool
Determine the most appropriate tool for vegetation management, first considering the mechanical methods listed on page 10 of the IVMP.
If it is determined that use of an herbicide is the best course, choose the most effective herbicide from Table 1 of the IVMP (page 12), based on vegetation type, herbicide selectivity, available equipment, aquatic considerations, and minimizing risks to human health and the environment. The selected control method should effectively kill the plant and eliminate the seed bank within a reasonable timeframe while avoiding undesirable consequences to non-target species.

## Slide 6: Step 3: Make a detailed plan
  Consider the potential costs associated with your project and the resources and personnel you will have and/or work with to complete the task. Then, write a plan that includes:
  A brief written description of the proposed work, including the target pest, number of applicators, application methods/procedures, selected IVMP-listed herbicide, transportation method(s), protective equipment, intended application window (based on the vegetative lifecycle), emergency response equipment, mixing and loading procedures, and cleaning and disposal procedures
  GPS locations (lat./long.)
  Extent of the proposed work (e.g. one linear mile with GPS data at end points or a 50 foot radius around one GPS point)
  Roadway name and mile posts or mile points
  Side(s) of road/direction of travel
  A map or Google Earth image with project site marked
  The location(s) where the herbicide(s) will be mixed and loaded
  A copy of the written emergency spill response plan

## Slide 7: Step 4: Communicate with DOT&PF M&O environmental staff
Contact the environmental staff for the region in which you wish to work. Explain your proposed work and submit your detailed work plan. Schedule a site visit with an M&O environmental staff member to inspect for aquatic sites within the proposed application area. It may take time before the environmental staff member can visit each proposed area.
Bear in mind that site conditions may change and a scheduled site visit may not reflect what is typical for the area. A site assessment must be conducted by the applicator on the day(s) of application both to determine if conditions are appropriate to apply herbicides and to identify any wet areas requiring a minimum 50 foot buffer (further as stated on pesticide label).

## Slide 8: Step 5: Start the pre-application checklist
One checklist will suffice for multiple sites along the same roadway, as long as each site is listed with location information. Sites at multiple airports require a separate checklist (and IVMP process) for each airport.

## Slide 9: Step 6: Contact the DOT&PF Right-of-Way (ROW) section to apply for a permit
The pre-application checklist requires that you apply for a permit that provides you with permission to work in the DOT&PF ROW. To obtain a permit, contact your regional ROW section (Central Region: 269-0700) and submit an application for a lane closure permit. Permits are required even for short-term, mobile operations that do not impact traffic. A traffic control plan detailing how far work will be from the road shoulder, what signs will be posted, and what work/actions are not permitted must be submitted with the permit application.

## Slide 10: Step 7: Notify the public and ADEC
To complete the pre-application checklist, you must notify these entities:
1. Notify the public via two consecutive public notice newspaper ads in the area (local and general) of the proposed application in accordance with 18 AAC 90.640. Ads must include the application location(s), complete herbicide name and EPA registration number of the herbicide, target pest(s), application method(s), approximate number of anticipated applications, and where the public can receive more information. The final ad must be circulated no later than 30 days prior to the first application date. One ad may suffice for multiple locations, so long as all locations are listed in the ad.
2. If the application will occur within 200 feet of a public water system, notification must be provided by mail, return receipt requested, to the owner of the public water system no later than 30 days before the application, or 30 days before the first application of a multi-application project.
3. Notify ADEC via email no later than 15 days prior to the date of any application so that the information can be posted to their website. Notification is required before each application of a multi-application project. Mike Coffey must be cc’d – Mike.Coffey@alaska.gov
4. If applying herbicides within the Municipality of Anchorage, notice must be given to the MOA at least 48 and no more than 120 hours in advance of spraying.*
*Note: The MOA has additional signage requirements as well. See Anchorage Pesticide Ordinance 15-75, 15.75.060

## Slide 11: Step 8: Submit the completed pre-application checklist with required paperwork
The completed pre-application checklist and all required backup paperwork must be submitted before herbicide application is approved by DOT&PF. Required paperwork includes:
A copy of the ROW permit and associated ROW documents
A copy of the email notifying ADEC of herbicide application
Copies of the final newspaper ads and affidavits demonstrating public notification
A copy of the certification card(s) of the certified applicator(s)
A statement indicating the name and address of each applicator, the category of use for which each applicator is certified, the company name and address where the pesticide was purchased, and the amount purchased and date of sale of the selected pesticide
Proof of liability insurance
Copies of email correspondence with the owner of the affected public water system, if applicable
Copies of additional permits/authorizations that have been obtained (e.g. APDES permit or ADEC Pesticide Use permit*)
* Note: An ADEC Pesticide Use permit and an Alaska Pollutant Discharge Elimination System (APDES) Pesticides General Permit are required prior to any aquatic application(s). Additionally, regional setbacks may be established for applications adjacent to aquatic sites.

## Slide 12: Step 9: Implement plan once approved, documenting work as it performed
Only after you receive a formal email of approval from Mike Coffey, the DOT&PF IVMP Person in Charge, can you begin herbicide application. All herbicide applications must comply with state and federal regulations and must be performed by certified applicators using DOT&PF IVMP-listed herbicides in accordance with their labels, the DOT&PF IVMP, and any regional guidelines. You must contact DOT&PF M&O environmental personnel if site or weather conditions or application dates or procedures change for any reason.
Make sure to have the DOT&PF field log on-site to record daily application rates, herbicide volumes, concentrations, treated acreage, and weather conditions.
Make sure to post warning signage as mandated in 18 AAC 90.630 at each point of access (and at intervals along the roadway for long linear applications) to the application area before applying herbicides. Warning signage must be posted for at least 24 hours and must remain posted through the restricted entry interval.

## Slide 13: Step 10: Complete and submit the post-application checklist
Complete and submit the post-application checklist and DOT&PF field log within 30 days of conducting herbicide application.

## Slide 14: Step 11: Required follow up
Per page 13 of the IVMP, post herbicide application follow up is required to assess the results of each application.
Application Location | Post-treatment Monitoring
Road ROW zones 1-3 | Site must be inspected within one month
FAA certified airports | Site must be inspected within one month
Uncertified airports | Site must be inspected within six hours

## Slide 15: Step 12: Recordkeeping
Both Mike Coffey and all involved certified pesticide applicators must keep accurate written records as described in 18 AAC 90.415 of all applications of general and restricted use pesticides within the DOT&PF ROW for a minimum of two years after each application.
For each herbicide applied to more than 20 acres in a calendar year, DOT&PF will publish a report on their website containing the complete product name, herbicide EPA registration number, the quantity of mixed herbicide applied, and the location of each application.

## Slide 16: Done!

## Slide 17: Questions?
Contact Info:
Renée Goentzel
Central Region M&O Environmental Analyst III
Jennifer Micolichek
Central Region M&O Environmental Analyst III