## Slide 1
Discussion of changes to stormwater management requirements, per the new APDES permit, issued by ADEC effective August 1, 2015.
2015 Alaska Pollutant Discharge Elimination System Permit
Presentation by:
Kristi Bischofberger, MOA Watershed Manager
Janie Dusel, PE, AWR Engineering

## Slide 2
APDES Permit Background
The APDES permit regulates stormwater discharge within the boundary of the MOA from the Municipal Separate Storm Sewer System (MS4) owned/operated by the MOA and ADOT&PF.
The MOA and ADOT&PF are co-permittees for the program.
The program is authorized by the National Clean Water Act, and managed by the State of Alaska Department of Environmental Conservation.

## Slide 3
Stormwater Treatment (Permit section 3.2.1)
        Treatment of runoff generated from the first 0.52 inches of rainfall through the use of LID or green infrastructure (GI) is required for projects that disturb 10,000 square feet of land or more, unless GI is determined to be infeasible.
        Treatment options include canopy interception, soil amendments, evapotranspiration, rainfall harvesting, engineered infiltration, extended filtration, and/or combination of these.
        MOA has developed draft criteria for a suite of “tools” to assist with meeting this requirement.
            Bioretention
            Filtration
            Infiltration, etc.
Highlights of this Permit for DOT projects

## Slide 4
Structural Stormwater Controls | RUNOFF |  | SUITABLE TO MEET SW MANAGEMENT REQUIREMENT |  |  | IMPLEMENTATION CONSIDERATIONS |  | 
 | Rate Control | Volume Reduction | Green Infrastructure Treatment |  | Detention and Peak Flow Control | Accepts Hotspot Runoff | Separation from Groundwater5 (feet) | Separation from Drinking Water Mains (feet)
Bioretention Facilities | Moderate | Moderate | ü |  | ü | Yes3 | 26 | 0
Soakaway Pits | Moderate | High | ü |  | ü | No7 | 2 | 10
Infiltration Basins | Moderate | High | ü |  | ü | No7 | 2 | 10
Infiltration Trenches | Moderate | High | ü |  | ü | No7 | 2 | 10
Vegetative Swales | Moderate | Moderate | ü |  | ü | No7 | 2 | 0
Pervious Pavement | Moderate | High | ü |  | ü | No | 2 | 10
Chamber Systems | High | High | ü |  | ü | No7 | 2 | 10
Wet Ponds | High | Low | ü |  | ü | No7 | N/A | 10
Dry Ponds | High | Low1 | *3 |  | ü | No7 | N/A | 10
Filter Strips | Low - Moderate2 | Low – Moderate2 | ü |  | ü | No7 | 2 | 0
Constructed Wetlands | Moderate - High | Moderate | ü |  | ü | Varies3 | N/A | 10
Natural Vegetation Retention/ Tree Canopy | Low-Moderate | Low-Moderate | ü |  |  | No7 | N/A | N/A
Landscaped Depressions | Moderate | Moderate | ü |  | ü | No7 | 2 | N/A
Sedimentation Basins | High | Low | ü |  | ü | No7 | 2 | 10
(1) May provide some volume reduction depending on permeability of native soil. (2) Increased performance when level spreaders are incorporated into the design. (3) Yes, under specific conditions. See design criteria section for further detail. (4) Hotspot runoff still requires treatment. |  |  |  | (5) Minimum separation distance between the seasonal high groundwater table elevation and the bottom of structural stormwater controls. (6) Modifications are available for locations with high groundwater. See specific design criteria section for further detail. (7) May be allowable with appropriate pre-treatment. |  |  |  | 

## Slide 5
Stormwater Treatment (Permit section 3.2.1)
        “Tools” have been developed to provide flexibility for site constraints:
          Poorly infiltrating soils, high groundwater, lack of surface space, etc.
        20% Area Allowance – Allows runoff from up to 20% of the site or 20% of impervious surface to be untreated by providing treatment of additional volume elsewhere onsite.
        Roadways with ROW widths less than or equal to 60 feet are not required to use GI.
Highlights of this Permit for DOT projects

## Slide 6
Stormwater Treatment (Permit section 3.2.1)
        If GI is not feasible, extended detention and alternative water quality treatment may be substituted.
        Infeasibility cannot be based solely on cost or difficulty.
        Infeasibility is usually the result of multiple constraining elements. (E.g. surface space AND high groundwater.)
Highlights of this Permit for DOT projects

## Slide 7
Stormwater Treatment (Permit section 3.2.1)
        The MOA has developed an Infeasibility Determination form.
        Separate forms for Site Design vs. Roadways
            Form guides the designer through site conditions and other constraints that might preclude the use of GI.
        This form is also used to meet the requirements of Permit section 3.2.3.5 Repair of Public Streets Roads and Parking Lots.
              Requires evaluation and documentation of the feasibility of incorporating runoff reduction techniques for projects that repair public streets, roads, or parking lots.
Highlights of this Permit for DOT projects

## Slide 8
Owner, Project, and Contact Info
Roadways
New or Redevelopment
Site Info:
Soil type
Percolation rate
Depth of GW table
ROW width
Width of Improvements
Sketch of structural section

## Slide 9
Types of facilities considered
and
Modifications considered
Site sketch
Description of why GI is not feasible

## Slide 10
Signature of Engineer
MOA Approval/Disapproval or Request additional info

## Slide 11
LID Strategy and Demonstration Projects (Section 3.2.3)
        Requires construction and performance evaluation of LID/Green Infrastructure demonstration projects. (Must be included in the 4th year annual report, summer of 2019)
        Three demonstration or “pilot” projects must be ADOT&PF owned projects.
            Projects must manage runoff from at least 10,000 square feet.
            Two (of the total of 5) projects must manage runoff from an area greater than five acres.
            One must be located in the Chester Creek, Fish Creek, Campbell Creek, or Little Campbell Creek watersheds.
Highlights of this Permit for DOT projects

## Slide 12
Questions?