## ITEM D-702	SLOTTED DRAINS

DESCRIPTION

702-1.1 This item shall consist of the construction of steel slotted drains according to these Specifications and in reasonably close conformity with the lines and grades shown on the Plans. Typical details shall be shown on the Plans.

MATERIALS

702-2.1 GENERAL. All slotted drains shall meet the requirements shown on the Plans and specified below.  All slotted drains shall meet specified hydraulic design requirements and shall support the loadings specified.

Standard details can be found in the American Association of State Highway and Transportation Officials (AASHTO)-AGC-ARTBA publication “A Guide to Standardized Highway Drainage Products.” All products used shall meet the most demanding aircraft loading and tire pressure requirements, as well as maintenance and equipment loadings.

702-2.2 PIPE.

- Steel slotted Drain. Pipe shall be metallic coated (galvanized or aluminized steel type II) corrugated steel type I meeting the requirements of AASHTO M 36. Pipe diameter and gage shall be as shown on the Plans.  The corrugated steel pipe shall have a minimum of two rerolled annular ends.

- Not Used.

702-2.3 GRATES AND CASTINGS.

- Steel Slotted Drain. Grates shall be manufactured from ASTM A36 or ASTM A1011, Grade 36 steel. Spacers and bearing bars (sides) shall be 3/16-inch material. The spacers shall be welded to each bearing bar with four 1-1/4-inch long by 3/16-inch wide fillet welds on each side of the bearing bar at spacings not exceeding 6 inches. The grates shall be 6 inches high or as shown on the Plans and shall have a maximum 1-3/4-inch opening in the top.

Grates shall be galvanized according to AASHTO M 111 except with a 2 ounces per square foot galvanized coating.

The grates shall be fillet welded to the corrugated steel pipe with a minimum weld 1 inch long on each side of the grate at every other corrugation. Weld areas and the heat affected zones where the slot is welded to the corrugated pipe shall be thoroughly cleaned and painted with a zinc-rich paint according to repair of damaged coatings in AASHTO M 36.

Each 20-foot length of drain delivered to the job site shall be within the following tolerances: vertical bow ± 3/8-inch, horizontal bow ± 5/8-inch, twist ± 1/2-inch.

- Not used.

702-2.4 CONCRETE. Plain or reinforced concrete used for steel slotted shall conform to the requirements of Section P-610 Concrete for Miscellaneous Structures.

CONSTRUCTION METHODS

702-3.1 EXCAVATION. The width of the trench shall be sufficient to permit satisfactory installation and jointing of the slotted drain and placing of a concrete backfill material under and around the drain, but shall not be less than the external pipe diameter plus 6 inches on each side. The depth of the trench shall be a minimum of 2 inches below the invert for steel slotted drain.

702-3.2 INSTALLATION. Slotted drains shall be laid in sections joined firmly together with coupling bands or as shown on the Plans. The top of all drains shall be held firmly in place to the proper grade, to preclude movement during the backfilling operation.

702-3.3 JOINING. Slotted steel drain joints shall be firmly joined by modified hugger type bands, or as indicated, to secure the pipe and prevent infiltration of the backfill. When the slotted steel drain is banded together, the adjacent grates shall have a maximum 3-inch gap.

702-3.4 BACKFILLING. Slotted drains shall be inspected before any backfill is placed. Damaged drains shall be aligned or replaced at the expense of the Contractor.

The trench holding the slotted drain assembly shall be backfilled with concrete that will easily flow under and around the drain and the trench wall. The opening in the top of grates shall be covered to prevent unwanted material from entering the drain during the backfilling and subsequent surfacing operations.

METHOD OF MEASUREMENT

702-4.1 The length of slotted drain will be measured in linear feet of slotted drain in place, completed, and approved. It will be measured along the centerline of the drain from end or inside face of structure to the end or inside face of structure, whichever is applicable. The classes, types, and sizes will be measured separately. All fittings will be included in the length as typical pipe sections being measured.

BASIS OF PAYMENT

702-5.1 Payment will be made at the contract unit price per linear foot for each kind of slotted drain type and size designated and at the contract unit price per cubic yard of concrete for backfill.

Payment will be made under:

Item D702.010.0000	Slotted Drain, 18-inch, 14 Gauge Pipe – per linear foot

Item D702.020.0000	Concrete for Backfill – per cubic yard

Item D702.030.0000	Trench Drain – per linear foot

MATERIAL REQUIREMENTS

AASHTO M 36	Corrugated Steel Pipe, Metallic-Coated, for Sewers and Drains

AASHTO M 111	Zinc (Hot-Dip Galvanized) Coatings on Iron and Steel Products

ASTM A36	Structural Steel

ASTM A1011	Steel, Sheet and Strip, Hot-Rolled, Carbon, Structural, High-Strength Low Alloy, High Strength Low Alloy with Improved Formability, and Ultra High Strength

Information	A Guide to Standardized Highway Drainage Products disseminated under the sponsorship of the American Association of State Highway and Transportation Officials, Associated General Contractors, and the American Road and Transportation Builders Association