## ITEM D-752	CONCRETE CULVERTS, HEADWALLS,
AND MISCELLANEOUS DRAINAGE STRUCTURES

DESCRIPTION

752-1.1 This item shall consist of plain or reinforced concrete culverts, headwalls, and miscellaneous drainage structures constructed according to these Specifications, at the specified locations and conforming to the lines, grades, and dimensions shown on the Plans or required by the Engineer.

MATERIALS

752-2.1 CONCRETE. Concrete shall meet the requirements of Item P-610.

CONSTRUCTION METHODS

752-3.1 UNCLASSIFIED EXCAVATION.

- Trenches and foundation pits for structures or structure footings shall be excavated to the lines and grades or elevations shown on the Plans. The excavation shall be of sufficient size to permit the placing of the full width and length of the structure or structure footings shown. The elevations of the bottoms of footings, as shown on the Plans, shall be considered as approximate only; and the Engineer may order, in writing, changes in dimensions or elevations of footings necessary to secure a satisfactory foundation.

- Boulders, logs, or any other objectionable material encountered in excavation shall be removed. All rock or other hard foundation material shall be cleaned of all loose material and cut to a firm surface either level, stepped, or serrated, as directed by the Engineer. All seams or crevices shall be cleaned out and grouted. All loose and disintegrated rock and thin strata shall be removed. When concrete is to rest on a surface other than rock, special care shall be taken not to disturb the bottom of the excavation, and excavation to final grade shall not be made until immediately before the concrete or reinforcing steel is to be placed.

- The Contractor shall do all bracing, sheathing, or shoring necessary to perform and protect the excavation and the structure as required for safety or conformance to governing laws. The cost of bracing, sheathing, or shoring shall be included in the unit price bid for excavation.

- All bracing, sheathing, or shoring shall be removed by the Contractor after the completion of the structure. Removal shall not disturb or mar finished concrete. The cost of removal shall be included in the unit price bid for excavation.

- After each excavation is completed, the Contractor shall notify the Engineer. No concrete or reinforcing steel shall be placed until the Engineer has approved the depth of the excavation and the character of the foundation material.

752-3.2 BACKFILLING.

- After a structure has been completed, backfill with approved material, in horizontal layers not to exceed 8 inches in loose depth, and compact. The field density of the compacted material shall be at least 95% of the maximum density. The maximum density shall be determined according to ATM 207 or ATM 212. The field density and moisture content shall be determined according to ATM 213.

- No backfilling shall be placed against any structure until approved by the Engineer. For concrete, approval shall not be given until the concrete has been in place 7 days, or until tests establish that the concrete has attained sufficient strength to withstand any pressure created by the backfill or the placement method.

- Fill placed around concrete culverts shall be deposited on each side at the same time and to approximately the same elevation. All slopes bounding or within the areas to be backfilled shall be stepped or serrated to prevent wedge action against the structure.

- Backfill will not be measured for direct payment. Performance of this work shall be considered as a subsidiary obligation of the Contractor, covered under the contract unit price for "unclassified excavation for structures."

752-3.3 WEEP HOLES. Weep holes shall be constructed as shown on the Plans.

752-3.4 Not Used.

METHOD OF MEASUREMENT

752-4.1 Unclassified excavation for structures will be measured in original position, between vertical planes 18 inches outside of and parallel to the neat lines of the footings.

752-4.2 Concrete will be measured by the dimensions shown on the Plans or approved by the Engineer, complete in place and accepted. No measurements or other allowances will be made for forms, false work, cofferdams, pumping, bracing, expansion joints, or finishing of the concrete. No deductions will be made for the volumes of reinforcing steel or embedded items.

752-4.3 Reinforcing steel will be measured by the theoretical weight shown on the Plans, complete in place and accepted. The unit weight used for deformed bars will be the weight of plain square or round bars, as the case may be, of equal nominal size.

BASIS OF PAYMENT

752-5.1 Payment will be made at the contract unit price per cubic yard for unclassified excavation for structures; at the contract unit price per cubic yard for concrete for the structures; and at the contract unit price per pound for reinforcing steel.

Payment will be made under:

Item D752.010.0000	Unclassified Excavation for Structures – per cubic yard

Item D752.020.0000	Structural Concrete – per cubic yard

Item D752.030.0000	Reinforcing Steel – per pound

Item D752.040.0000	Trench Drain – per linear foot

TESTING REQUIREMENTS

ATM 212	Standard Density of Coarse Granular Materials Using the Vibratory Compactor

ATM 207	Moisture-Density Relations of Soils

ATM 213	In-Place Density and Moisture Content of Soil and Soil-Aggregate by Nuclear Methods