## ITEM F-174	SINGLE AND DOUBLE POLE SWING GATE

DESCRIPTION

174-1.1 Furnish and install single or double pole swing gates at the locations and according to the details shown on the plans. Include gate foundations, gate assemblies, installation, application of reflective tape, and all materials and incidentals necessary for complete and operational gates.

MATERIALS

174-2.1 STEEL. Provide structural steel that conforms to the requirements of ASTM A36 (Standard specification for carbon structural steel). Use structural steel galvanized in conformance with ASTM A123 (standard specification for hot dipped galvanized zinc coatings on iron and steel products) 2.0 OZ/SF, or in conformance with ASTM A153 (standard specification for hot dip galvanized zinc coatings on iron and steel hardware) as appropriate. Galvanize gates and gate components after fabrication. Make repairs to damaged galvanizing in conformance with ASTM A780 (standard practice for repair of damaged and undercoated areas of hot dip galvanized coatings). Provide high strength bolt, nut and washer material conforming to the requirements of ASTM A325. Provide galvanized heavy hex-type bolts and nuts if components connected are galvanized. Provide galvanized machine bolts conforming to ASTM A307.

174-2.2 CONCRETE. Provide concrete of a commercial grade with a minimum 28-day compressive strength of 2,500 psi or an approved, pre-mixed, sacked concrete.

174-2.3 LOCKS. Provide brass restricted keyway padlocks for each gate with a shackle that is 3/8-inch in diameter and a closed clearance of 2-1/4 inches. Provide locks with control key removable cores and furnish a separate replacement core for each lock. Provide cores that are keyed differently. Provide 4 keys per lock, and 2 core-removable keys.

174-2.4 REFLECTIVE MARKINGS. High intensity reflective sheeting per ASTM D4956.

CONSTRUCTION REQUIREMENTS

174-3.1 FABRICATION. Give 15 days notice before beginning fabrication work at the shop so that inspection may be provided.

Provide workmanship and finish equal to the best practice in modern fabrication shops. Finish portions of the work exposed to view neatly. Perform shearing, flame cutting, and chipping carefully and accurately. Steel or wrought iron may be flame cut, provided a smooth surface is obtained by the use of a mechanical guide. Perform flame cutting by hand only where approved, and smooth the surface by planing, chipping, or grinding. Adjust and manipulate the cutting flame so as to avoid cutting beyond the prescribed lines. Fillet re-entrant cuts to a radius of not less than ¾-inch.

Finishing and Shaping: Provide finished members true to line and free from twists, bends, and open joints. Store structural material, either plain or fabricated, at the fabricating shop above the ground on platforms, skids, or other supports. Keep free from dirt, grease, or other foreign matter, and protect from corrosion.

Perform welding in accordance with AWS D1.1.

174-3.2 INSTALLING POSTS. Set all gate posts in concrete at the required dimensions and depths and at the spacing shown on the plans.

Properly align post holes so that there is a minimum of 3 inches of concrete on all sides of the posts. Thoroughly compact concrete around each post by tamping or vibrating and finish to a smooth surface slightly higher than the surrounding ground and sloped to drain away from the posts. Set all posts plumb and to the required grade and alignment. Do not install materials on the posts or disturb the posts within 7 days after completion of the individual post footing.

Should rock be encountered at a depth less than the planned embedment depth, drill a hole 2 inches larger than the greatest dimension of the post and to a depth of 12 inches below the planned embedment depth. After the posts are set, fill the remainder of the drilled hole with grout, composed of one part Portland cement and two parts mortar sand. Fill any remaining space above the rock with concrete in the manner described above. In lieu of drilling, the rock may be excavated to the required embedment depth.

174-3.3 INSTALLING GATES. Install gates level and plumb with the swing as indicated on the plans. Install reflective sheeting on clean, dry surfaces in accordance with the manufacturer’s recommendations.

METHOD OF MEASUREMENT

174-4.1 By the number of gates of each type installed and accepted.

BASIS OF PAYMENT

174-5.1 Payment will be made at the contract unit price for each furnished, installed and accepted item.

Payment will be made under:

Item F174.010.____	Single Pole Swing Gate, ____-feet Wide – per each

Item F174.020.____	Double Pole Swing Gate, ____-feet Wide – per each