## ITEM G-700	TRAFFIC CONTROL FOR AIRPORTS

DESCRIPTION

700-1.1 Provide suitably equipped airport flagger(s) with no other assigned duties to monitor and control the Contractor’s personnel and equipment crossing or occupying any portion of the Air Operations Area of the airport, as required under Section 80-04 Limitation of Operations. The airport flagger shall have no other assigned duties.

REQUIREMENTS

700-2.1 Furnish airport flaggers and all necessary equipment. Equip each airport flagger assigned to an aircraft operations area with a two-way radio that broadcasts and receives on the designated Common Traffic Advisory Frequency (CTAF) for the project airport as found in the Alaska Supplement of the United States Government Flight Information Publication. Provide each airport flagger with a two-way radio to contact construction equipment and other airport flaggers on the project. Equip each airport flagger for vehicular traffic control with a flagging paddle that conforms to the requirements of the Alaska Traffic Manual.

Locate each airport flagger at a position as shown on the Plans or as described in the Safety Plan, or at an alternate location as directed by the Engineer. Ensure that each airport flagger maintains their assigned post at all times. Airport flagger positions will be adjusted as conditions warrant.

METHOD OF MEASUREMENT

700-4.1 Airport flagger will be measured by the hour for the actual number of hours that each airport flagger performed as directed by the Engineer.

BASIS OF PAYMENT

700-5.1 Payment will be made at the contract unit price for each Airport Flagger per hour. The hourly rate for Airport Flagger is set at [$__.__] per hour for this contract. The Engineer does not require a change order/directive for this pay item.

Payment will be made under:

Item G700.010.0000	Airport Flagger – per contingent sum

# Comments

Note to Designer:  CTAF is not the correct frequency for airports with a control tower. Consider whether CTAF is the appropriate frequency for your airport project.

Note to Designer: Input the current flagger rate.

https://dot.alaska.gov/stwddes/dcsconst/index.shtml#resources