## ITEM G-705	WATERING FOR DUST CONTROL

DESCRIPTION

705-1.1 Furnish all equipment and labor necessary to supply watering for dust control as required by the approved traffic control plans or as directed by the Engineer. This item is for dust control outside of the construction work area. Dust control within the work area is incidental to the contract and no separate payment will be made.

REQUIREMENTS

705-2.1 WATERING. Furnish, haul, and place water for dust control as directed. Use water trucks capable of adjusting the rate of water flow from the operator’s position. Distribute a light-water spray pumped from a tanker in a uniform spray pattern to cover a minimum 30 foot width in one pass and without causing erosion. Gravity flow will not be allowed. The Engineer will control water application.

If you take water from a lake, stream, or other natural water body, first obtain a water removal permit from the Alaska Department of Natural Resources (DNR). Comply with the Alaska Department of Fish and Game and/or DNR Office of Habitat Management and Permitting screening requirements for all water removal operations.

METHOD OF MEASUREMENT

705-4.1 By the 1,000 gallons (M-gallon) of water applied. The water will be measured by means of calibrated tanks or distributors, accurate water meters, or by weighing. If by weight, convert to gallons at 8.34 pounds per gallon. If by volume, convert to gallons at 7.48 gallons per cubic foot.

BASIS OF PAYMENT

705-5.1 The contract price includes all resources required to provide watering, as directed.

Payment will be made under:

Item G705.010.0000	Watering for Dust Control – per Mgal

# Comments

Note to Designer: If using this specification and G-710, remove the contingent rate for watering from G-710.