## ITEM P-151	CLEARING AND GRUBBING

DESCRIPTION

151-1.1 This item shall consist of clearing or clearing and grubbing, including the disposal of materials, for all areas within the limits designated on the Plans or as required by the Engineer.

Clearing shall consist of the cutting and removal of all trees, stumps, brush, logs, hedges, the removal of fences and other loose or projecting material from the designated areas. The grubbing of stumps and roots will not be required.

Clearing and grubbing shall consist of clearing the surface of the ground of the designated areas of all trees, stumps, down timber, logs, snags, brush, undergrowth, hedges, heavy growth of grass or weeds, fences, structures, debris, and rubbish of any nature, natural obstructions or such material which in the opinion of the Engineer is unsuitable for the foundation of strips, pavements, or other required structures, including the grubbing of stumps, roots, matted roots, foundations, and the disposal from the project of all spoil materials resulting from clearing and grubbing by burning or otherwise.

Selective tree removal requires the hand cutting (topping) of all types of trees either by chain saw or by other approved conventional hand clearing methods. Dispose of the tree in the same manner as clearing and grubbing spoil materials.

CONSTRUCTION METHODS

151-2.1 GENERAL. The areas to be cleared or cleared and grubbed shall be staked or otherwise marked on the ground at the direction of the Engineer. The Engineer will flag or mark each tree designated for selective tree removal. The clearing and grubbing shall be done far enough ahead of the earthwork operation to permit cross-sectioning prior to excavation or embankment. Mechanical brush cutting equipment may be used for clearing. Dozers or other mechanical equipment not specifically designed for brush cutting may not be used.

Vegetation clearing will follow the USFWS Recommended Time Periods for Avoiding Vegetation Clearing in Alaska in order to protect Migratory Birds unless the USFWS has been consulted to determine the most appropriate method to avoid impacts to nesting birds.

Debris from mechanical brush cutting equipment less than 4 feet long by 4 inches in diameter may remain in place outside of Runway and Taxiway Safety Area surfaces except as specified in areas to be embanked. All other spoil materials generated by clearing or by clearing and grubbing shall be disposed of by burning, when permitted by local laws, or by removal to approved disposal areas. When burning of material is permitted, it shall be burned under the constant care of competent watchmen so that the surrounding vegetation and other adjacent property will not be jeopardized. Burning shall be done according to all applicable laws, ordinances, and regulations. Before starting any burning operations, the Contractor shall notify the agency having jurisdiction.

As far as practicable, waste concrete and masonry shall be placed on slopes of embankments or channels. When embankments are constructed of such material, this material shall be placed according to requirements for formation of embankments. Any broken concrete or masonry which cannot be used in construction, and all other materials not considered suitable for use elsewhere, shall be disposed of by the Contractor. In no case shall any discarded materials be left in windrows or piles adjacent to or within the airport limits. The manner and location of disposal of materials shall be subject to the approval of the Engineer and shall not create an unsightly or objectionable view. When the Contractor is required to locate a disposal area outside the airport property limits, the Contractor shall obtain and file with the Engineer, permission in writing from the property owner for the use of private property for this purpose.

If the Plans or the Specifications require the saving of merchantable timber, the Contractor shall trim the limbs and tops from designated trees, saw them into suitable lengths, and make the material available for removal by others.

Perform blasting in accordance with all Federal, state, and local safety regulations. Submit notice 15 days prior to starting work. Submit a Blasting Plan, prepared and sealed by a registered professional Engineer that includes calculations for overpressure and debris hazard. Obtain written approval prior to performing any blasting and notify the Engineer 24 hours prior to blasting. Include provisions for storing, handling and transporting explosives as well as for the blasting operations in the plan. The Contractor is responsible for damage caused by blasting operations.

The Contractor shall remove existing structure and utilities that are identified to be removed or demolished, except when another entity is identified in the Contract to accomplish the work.

151-2.2 CLEARING. The Contractor shall clear the staked or indicated area of all objectionable materials. Trees unavoidably falling outside the specified limits must be cut up, removed, and disposed of in a satisfactory manner. In order to minimize damage to trees that are to be left standing, trees shall be felled toward the center of area being cleared. The Contractor shall preserve and protect from injury all trees not to be removed. The trees, stumps, and brush shall be cut flush with the original ground surface. The grubbing of stumps and roots will not be required.

Fences shall be removed and disposed of when directed by the Engineer. Fence wire shall be neatly rolled and the wire and posts stored on the airport if they are to be used again, or stored at a designated location if the fence is to remain the property of a local owner.

151-2.3 CLEARING AND GRUBBING. In areas designated to be cleared and grubbed, all stumps, roots, buried logs, brush, grass, and other unsatisfactory materials shall be removed, except where embankments exceeding 4 feet in depth are to be made in areas that are not subject to aircraft or vehicle traffic loadings and are unpaved.   For embankments that are greater than 4 feet in depth, which are not subject to aircraft or vehicle traffic loadings and are unpaved, all unsatisfactory materials shall be removed, but sound trees, stumps, and brush can be cut off flush with the original ground and allowed to remain. Tap roots and other projections over 1.5 inches in diameter shall be grubbed out to a depth of at least 18 inches below the finished subgrade or slope elevation.

Any buildings and miscellaneous structures that are shown on the Plans to be removed shall be demolished or removed, and all materials therefrom shall be disposed of either by burning or otherwise removed from the site. The cost is incidental to this item. The remaining or existing foundations, wells, cesspools, and all like structures shall be destroyed by breaking down the materials of which the foundations, wells, cesspools, etc., are built to a depth at least 2 feet below the existing surrounding ground. Any broken concrete, blocks, or other objectionable material which cannot be used in backfill shall be removed and disposed of at the Contractor’s expense. The holes or openings shall be backfilled with acceptable material and properly compacted.

All holes remaining after the grubbing operation in embankment areas shall have the sides broken down to flatten out the slopes, and shall be filled with suitable material, moistened and properly compacted in layers to the density required in Item P-152. The same construction procedure shall be applied to all holes remaining after grubbing in excavation areas where the depth of holes exceeds the depth of the proposed excavation.

METHOD OF MEASUREMENT

151-4.1 Measure according to GCP Section 90 and the following:

- Acre. The area acceptably cleared, or cleared and grubbed, measured on the ground surface. Only areas shown on the Plans, or areas cleared at the Engineer’s direction will be measured. Islands of existing cleared areas, such as lakes, ponds, existing stream beds, and roads and trails within the clearing limits of more than 60 square yards will not be included as pay areas.

- Each. The number of designated trees acceptably removed, regardless of size.

BASIS OF PAYMENT

151-5.1 At the contract lump sum or unit price, for each of the pay items listed below that are shown in the bid schedule.

Payment will be made under:

Item P151.010.0000	Clearing – per acre

Item P151.020.0000	Clearing – per lump sum

Item P151.030.0000	Clearing & Grubbing – per acre

Item P151.040.0000	Clearing & Grubbing – per lump sum

Item P151.050.0000	Selective Tree Removal – per each