## ITEM P-163	SURFACE CLEANING

DESCRIPTION

163-1.1	Clean designated concrete areas to leave a sound and durable surface suitable for overlay. Collect all loose and friable material from unsound surfaces and crevices. Haul waste to the waste disposal site designated on the plans.

EQUIPMENT & MATERIALS

163-2.1 Provide the following equipment:

- Water sprayer rated and producing at least 3000 PSI.

- Truck-mounted sweeper with integrated vacuum unit.

Obtain approval for substitute equipment proposed for this work from the Engineer. Use equipment capable of leaving a sound surface without particulate residue.

Provide all water and other expendables necessary to complete the described work.

CONSTRUCTION REQUIREMENTS

163-3.1 Remove all loose and friable material from existing concrete. Collect all loosened particles and place them at the waste disposal site indicated in the plans. Sound and durable surfaces are those capable of withstanding a sustained application of the specified water spray with the nozzle placed against the concrete.

METHOD OF MEASUREMENT

163-4.1 Section 90. Surface cleaning areas will be determined by plan dimensions or as staked in the field.

BASIS OF PAYMENT

163-5.1 At the contract unit price for performing the work as described.

Payment will be made under:

Item P163.010.0000	Surface Cleaning – per square yard