## ITEM P-170 SOIL TESTING

DESCRIPTION

170-1.1 Characterize and test soils for hydrocarbon fuel and deicer compound contamination at the project site. The purpose of the testing is to assure the proper disposal of contaminated materials and to determine what soil will or will not need special handling. Employ an independent environmental consulting firm with Alaska Department of Environmental Conservation (DEC) approved personnel meeting 18 AAC 78 qualifications to perform work under this item.

REQUIREMENTS

170-2.1 GENERAL. The Engineer will direct implementation of the soil testing work along the fuel hydrant system piping and appurtenances and for other areas of the excavation if contaminated soils are encountered. Prior to commencing with soils excavation, submit a field sampling work plan for the soil sampling and testing procedures. Ensure that a qualified environmental consulting firm representative is available to perform work in accordance with DEC procedures during pavement/concrete removal, soil removal, and stockpiling.

The testing program as outlined requires cooperation between the Contractor and Consultant to achieve the results required by the Airport. If the Consultant deems that there is a safety problem, it will be the right of the Consultant to notify the Contractor of the issue. If corrective actions are not instituted by the Contractor, the Consultant must notify the State for corrective actions and negotiations to take place with the Contractor.

170-2.2 WORK PLAN. Based on the site’s historical information prepare a site specific field sampling plan for work to be performed under this item. Submit the plan to the Engineer, DEC, and the ASIG Environmental Manager allowing a minimum of 10 work days for review and approval of the field sampling plan. For planning purposes, classify fuel contaminated materials as:

- Clean. Diesel range organics (DRO) 0 to 250 parts per million (ppm) or gasoline range organics (GRO) 0 to 300 ppm.

- Contaminated. DRO greater than 250 ppm or GRO greater than 300 ppm. Further classify DRO contaminated materials as:

  - Warm. Contaminated soil greater than 250 ppm DRO and less than or equal to 12,500 ppm DRO.

(2)	Hot. Contaminated soil greater than 12,500 ppm DRO.

Soils will not be classified for deicer compound contamination.

170-2.3 SOIL TESTING AND DOCUMENTATION PROCEDURES. For areas that are excavated, determine if excavated soil is contaminated with hydrocarbon fuel and/or deicer compounds and classify the fuel contaminated materials for segregation and disposal as necessary. Conduct soil tests for deicer compound contamination only when required by DEC or when necessary to determine if deicer compound contamination is impacting field screening readings for fuel contamination.

Use DEC approved methods in accordance with the DEC Underground Storage Tank (UST) Procedures Manual, DEC Underground Storage Tank Regulations (18 AAC 78), and DEC Contaminated Site Regulations (18 AAC 75) to perform the following:

- Sampling Based on Field Screening Results. For excavated areas, use visual observation and conduct field screening using a photo-ionization detector (PID) or flame-ionization detector (FID) to determine the location of areas that could be contaminated and will require additional screening and sampling.

(1) Field Screening. From these areas with suspected contamination, determine sampling locations by field screening at a predetermined frequency for excavated soils and field screening the bottom of the excavation on a minimum 25-foot by 25-foot grid and the sidewalls at 25-foot intervals half way between the top and bottom of the excavation except that trench excavations for storm drains, fueling systems, utilities, etc. may be field screened at the centerline and both side walls at 25 foot intervals.

(2) Analytical Sampling and Testing. If soil is to be left in place, collect samples for laboratory analysis from 25% of the field screening locations with the highest reading. Analyze the samples for DRO and GRO/BTEX. Samples can also be analyzed for glycols per the field sampling plan. Collect one duplicate sample for every 10 samples collected. Locate and document all excavation samples by field surveying. Trench soils excavated for storm drains, fueling systems, utilities, etc. may be characterized prior to excavation using borings. Perform borings at 25-foot intervals along the proposed trench centerlines. Return test results to the Engineer within a minimum of 5 days after sampling.

(3) Storage Pile Sampling and Testing. Store potentially warm or hot soil in 30 to 50 cubic yard segments prior to determination of final disposal. Collect a soil sample from each segment of storage pile soil to be analyzed for DRO. Collect one duplicate sample per every 10 soil samples collected. Additional soil samples can be collected to be analyzed for glycols per the field sampling plan. Return test results to the Engineer within a minimum of 5 days after sampling.

Submit field and laboratory results to DEC (original hard copy, two copies, and electronic format) and the Engineer (one copy). Brief the Engineer on a daily basis as required. Prepare and submit a draft report to the ASIG Environmental Manager 15 business days after receipt of the analytical results. Submit a final project report to include all field and lab results to the DEC, the Engineer, and ASIG (original in hard copy and electronic format and six copies to DEC, one copy to the Engineer).

170-2.4 TRENCH PLUGS. Where required to inhibit fuel contamination migration, provide minimum 4-foot vertical trench plugs, extending 2 feet below and 2 feet above the utility installation, and bentonite/sand ratio of 20% bentonite to 80% sand by weight. Comply with the following material requirements:

- Bentonite. Pulverized, 55 lbs/ft3, 75% - 90% passing 75 micro-meter sieve, supplied in bags clearly marked to show weight, grade, and supplier.

b.	Sand. Meet ASTM C144 Mason Sand.

170-2.5 DISPOSITION OF SOILS.

- Clean Soils. Clean soils meeting material requirements may be re-used in the project. Move any excess clean soils without organics to the disposal area shown in the Plans. Move excess clean soils with organics to an off-airport disposal site in accordance with P-152.

- Hot Soils. Haul soil classified as hot to Alaska Soil Recycling facility located at 2301 Spar Avenue, Anchorage for thermal remediation. As an alternative, the Engineer may direct hot soil to be stockpiled in accordance with item P-171. When hot soil is identified, immediately contact the ANC Environmental manager through the Engineer. Prior to and after delivery of contaminated soils to the thermal remediation facility, weigh haul vehicles at Carlile Enterprises, 1813 E 1st Avenue, Anchorage. Present a certified invoice to the Engineer and a copy to the ANC Environmental manager. Coordinate delivery of contaminated soils with the remediation facility prior to the haul. The remediation facility will not accept soil without ANC Environmental and DEC’s approval. Coordinate with remediation and weigh facilities to determine limitations on the type of haul vehicle and comply with any limitations.

- Warm Soils. Segregate and store warm contaminated soil removed from the excavations separate from other project storage piles. Transport soil classified as contaminated warm directly to the landspreading area at the direction of the Engineer, unless re-used in accordance with DEC screening and analytical sampling requirements.

170-2.6 LANDSPREADING AND TEMPORARY CONTAMINATED SOIL STOCKPILE AREAS. Determine dimensions for temporary stockpiles. Clearly mark, map, and document soil lots within landspreading and temporary stockpile areas. Identify and delineate the stockpile and landspreading areas by field markings that are unaffected by the elements and designed for long term storage. Identify, document, and correlate all field markings to test results in the report document. Estimate and document quantities of material placed in the landspreading and temporary stockpile areas using truck counts.

METHOD OF MEASUREMENT

170-4.1 Subsection 90-05 and measured as specified in the directive authorizing the work.

BASIS OF PAYMENT

170-5.1 As specified in the directive authorizing the work and as follows.

For Soil Testing Program, payment for all labor (including the environmental consultant), equipment, and materials necessary to conduct sampling and testing, the screening of the area to be excavated, field testing and screening of excavated material including laboratory correlation, locating and documenting all excavation samples by field surveying, stockpile marking, mapping, and documentation to correlate soil lots to test results will be made in accordance with subsection 90-05 Compensation For Extra Work On Time And Materials Basis.

For Supplemental Laboratory Test, payment will be made in accordance with subsection 90-05 Compensation for Extra Work On Time and Materials Basis to furnish all labor, equipment, and materials necessary for additional composite or discrete sample tests ordered by the Engineer.

For “Hot” Material Offsite Transportation and Disposal, payment will be made in accordance with subsection 90-05 Compensation for Extra Work On Time and Materials Basis to furnish all labor, equipment, and materials necessary to transport and dispose of contaminated “hot” soil.

Field surveying to locate and document excavation samples will be paid for under the Soil Testing Program pay item. Field surveying to locate and document additional sample tests ordered by the Engineer will be paid for under the Supplemental Laboratory Test pay item.

Payment will be made under:

Item P170.020.0000	Soil Testing Program – per contingent sum

Item P170.040.0000	Supplemental Laboratory Test – per contingent sum

Item P170.080.0000	“Hot” Material Offsite Transportation and Disposal – per contingent sum