## ITEM P-171	TEMPORARY CONTAMINATED SOIL STOCKPILE AREA

DESCRIPTION

171-1.1 At the location shown on the plans or as directed by the Engineer, establish a temporary petroleum contaminated soil storage area and construct contaminated soil stockpiles according to the requirements for [specify short-term or long-term] stockpiling as defined in Alaska Department of Environmental Conservation (DEC) Contaminated Site Regulations (18 AAC 75) for [specify short-term or long-term] storage of petroleum contaminated soil. This area serves as temporary storage for material that has been designated fuel contaminated soil.

Nothing in this contract is intended to impose on the Contractor the status under state or federal law of a facility owner or operator or the status of an owner or generator of the hazardous substances or contaminated materials that existed on the designated sites before the contract. The Contractor must carefully abide by all applicable laws, regulations, plans and practices to avoid becoming a facility owner or operator, or an owner or generator of contaminated materials by a release of hazardous substances.

MATERIALS

171-2.1 BERM. Use uncontaminated suitable material from project excavations.

171-2.2 SUBMITTALS. At least 5 days before ordering liner and cover material, submit manufacturer’s product bulletins for approval. Include in the submittal proposed seam layout and joining methods, if applicable.

171-2.3 LINER. Use a membrane impervious to petroleum that meets the minimum specifications for [specify short-term or long-term storage] as per 18 AAC 75.370, Table D

171-2.4 COVER. Use 0.006 inch (6 mil) reinforced polyethylene for cover sheeting with manufacturer or field sealed seams.

171-2.5 TEMPORARY FENCE. Provide a 6-foot high chain-link fence on a tubular frame supported with concrete foundation blocks.

CONSTRUCTION REQUIREMENTS

171-3.1 CONTAMINATED CRITERIA. The applicable criteria for determining what soil is fuel contaminated and placed in this area is described in Item P-170 and P-152.

171-3.2 STOCKPILE AREA PREPARATION. Construct separate bermed areas for each stockpile by placing suitable material from unclassified excavation on a prepared site. Prepare site by removing objects that may damage the liner and grade to smooth contours.

171-3.3 LINER. Cover both the berm and the stockpile floor with the liner.

171-3.4 COVER. Lap the edge of the cover over the bottom liner to prevent water from running through the soil. Maintain the top cover over the stockpiled material. Secure sheeting against displacement throughout the project. Use rope, sandbags, and/or netting to secure the cover. Do not use tires.

171-3.5 TEMPORARY FENCE. Surrounding the completed temporary stockpiles, erect a 6-foot high fence.

171-3.6 REMOVAL. Remove berm, liner, cover and temporary fence following disposition of the temporarily stockpiled material.

METHOD OF MEASUREMENT

171-4.1 Subsection 90-05 Compensation For Extra Work On Time And Materials Basis and measured as specified in the directive authorizing the work.

BASIS OF PAYMENT

171-5.1 Subsection 90-05 Compensation for Extra Work on Time and Materials Basis and paid for as specified in the directive authorizing the work.

Payment will be made under:

Item P171.010.0000	Temporary Contaminated Soil Stockpile – per contingent sum

# Comments

Note to Designer: Insert the appropriate term.

Note to Designer: Insert the appropriate term.