## ITEM P-634	LONGITUDINAL JOINT REPAIR

DESCRIPTION

634-1.1 This work includes all labor, equipment and materials needed for paving, cold planing, and placing tack coat for the longitudinal pavement joints on the taxiway and apron, as detailed in the Plans.

MATERIALS

634-2.1 Longitudinal joint repair shall be accomplished using Hot Mix Asphalt, Type [__], Class [__], and Tack Coat [___] as specified in Items P-401 Asphalt Mix Pavements and P-603 Emulsified Asphalt Tack Coat.

CONSTRUCTION REQUIREMENTS

634-3.1 Cold plane existing longitudinal pavement joints to the width and depth specified in the plans. Place tack coat on the cold planed surface meeting requirements described in P-603-3.3. Place, spread and compact the asphalt concrete mix on the cold planed surface at the thickness called for in the plans, meeting the construction methods requirements of P-401.

METHOD OF MEASUREMENT

634-4.1 Longitudinal joint repair will be measured by the linear foot at the center of the joints.  All work and materials used in Item P634.010.0000, including those with separate bid items, are subsidiary and will not be measured separately for payment and will not be included in the Quality Level Analysis (QLA).

BASIS OF PAYMENT.

634-5.1 The accepted quantity will be paid for at the contract unit price for the pay items listed below, complete in place.

Payment for repairing joints will include labor, asphalt concrete mix (including oil), compaction, tack coat, cold planing, clean up, equipment, and other items necessary to complete the work as detailed in the plans.

Payment will be made under:

Item P634.010.0000	Longitudinal Joint Repair – per linear foot

# Comments

Note to Designer:  Add Type, Class, and Tack Coat per project.