## ITEM P-650	AIRCRAFT TIE-DOWN

DESCRIPTION

650-1.1 This item consists of furnishing and installing aircraft tie-down anchors according to these specifications and the details on the Plans, or as directed by the Engineer.

MATERIALS

650-2.1 GENERAL.

Meet the strength and/or capacity requirements of this section for the type of anchor specified.

Substitution of products as approved equals will be determined by comparing ratings for tensile breaking strength and pull-out capacity that exceed the specified minimums when installed under prevailing soil or rock conditions. The practicality of installing proposed anchors at the plan locations and corrosion resistance will also be considered.

Locate existing tiedowns and record their locations such that new tie-downs may be placed in a similar layout.

Cut existing tie-downs off at the lowest point available after excavation in the area is complete.

Install tie-downs such that the new tie-down is offset 18 inches or as directed by the Engineer to avoid hitting the existing anchor with the new installation.

650-2.2 SOIL ANCHOR TIE-DOWNS.

- Driven Toggle. Provide an anchor assembly with a minimum tensile breaking strength of 9,000 pounds, a minimum working load capacity of 3,500 pounds and a minimum field pull-out capacity of 5,000 pounds. Provide anchors equipped with stainless steel cable, swaged eyes at cable ends, and no intermediate connections.

- Buried Plate. Provide an anchor assembly meeting the details shown on the plans.

- Helical “Screw” Anchor. Provide an anchor assembly with minimum tensile breaking strength of 9,000 pounds, a minimum working load capacity of 3,500 pounds, and a minimum field pull-out capacity of 5,000 pounds.

For each anchor assembly, provide a chain extension to the anchor cable so that the cable eye is buried 12 inches minimum below finish grade and the chain extends several links above finish grade after locking the anchor. Use 3/8-inch grade 43 high test hot galvanized steel chain with two 3/8-inch removable coupling links, one at each end of the chain.

650-2.3 ROCK ANCHOR TIE-DOWNS. Rock anchors shall be 1/2-inch diameter Williams Solid Bar “Spin Lock” Rock Bolts, Williams Titan Injection Anchor 30/16, or an approved equal. Provide anchor assembly with a minimum tensile breaking strength of 9,000 pounds and minimum field pull-out capacity of 5,000 pounds. Provide chain and chain coupling links meeting the same requirements as specified for soil anchor tie downs.

650-2.4 TEMPORARY TIE-DOWNS. Temporary tie-down anchors shall provide a minimum 500 pounds of resistance to uplift per anchor. Temporary anchors shall be laid out as shown on the plans or as approved by the Engineer. Each anchor shall be provided with a 2-inch link or eye to which aircraft can be tethered. If above ground weights are used they shall be painted with reflective paint to be visible from any horizontal angle.

CONSTRUCTION METHODS

650-3.1 GENERAL. Soil and Rock Anchor tie-downs shall be installed as shown on the Plans.

Install anchor eye to the end of the anchor shaft by either bolting or as recommended by the manufacturer and approved by the Engineer. Eye must be able to pass a 1-inch rope or pin.

650-3.2 SOIL ANCHOR TIE-DOWNS.

              - Driven Toggle. Drive to sufficient depth to develop the minimum pull-out strength according to the manufacturer’s installation instructions. Predrilling may be required depending on soil class. Anchor placement shall be achieved by methods recommended in the manufacturer’s installation instructions. Backfill material, when required, shall be aggregate compacted to the satisfaction of the Engineer. If the anchor is set in pavement, backfill to a level 2-inchs below finish grade. Two-component sealant shall be used to fill the remainder of the hole to a level 1-inch below finish grade.

              - Buried Plate. Install each plate on a level and compacted surface at 5 feet minimum below finish grade. Place backfill with the chain plumb and under tension. Meet the material and compaction requirements for the applicable lift of material involved.

              - Helical “Screw” Anchor. Helical anchors shall be handled, stored, and installed in accordance with the manufacturer’s recommendations. The helix of the helical anchors shall be installed a minimum of 6 feet below finish grade. Under no circumstances shall the manufacturer’s recommended maximum allowable torque be exceeded at any time during installation.

The helix must be advanced in a continuous manner that allows the helix to “screw” into the soil matrix rather than “auger” through the soil matrix, resulting in disturbed soils around the helices. The rate of advance should provide a rotation of 5 to 15 rotations per minute. Apply uniform down pressure to maintain a penetration rate commensurate with the helix pitch. The rate of rotation and magnitude of down pressure may require adjustments during installation.

Prior to installing helical anchors in paved areas, core through the asphalt using a circular coring machine approved by the engineer. Install as shown on the Plans and compact to the satisfaction of the Engineer.

The helical anchors installed shall be field tension tested to the design pull-out load under the supervision of the Engineer to confirm tension load performance.

650-3.3 ROCK ANCHOR TIE-DOWNS. Rock anchors shall be anchored in sound bedrock at sufficient penetration to develop the minimum pull-out strength according to the manufacturer’s instructions.

650-3.4 TEMPORARY TIE-DOWNS. Temporary tie-downs shall be produced that can be located to provide tie downs for aircraft displaced by the Contractor’s operations. Tie-downs shall not require any permanent modifications to existing facilities or pavements and shall be re-locatable using readily available equipment. Initial placement and subsequent relocations of tie-downs shall be accomplished at the direction of the Engineer at no additional cost to the State.

650-3.5 MANUFACTURER’S CERTIFICATION AND ACCEPTANCE TESTING. For anchors where minimum tensile breaking strength or working load capacity is specified, provide manufacturer’s certification that requirements are met. For anchors where minimum field pull-out capacities are specified, provide an Engineer approved testing apparatus that can apply and measure the required minimum field pull-out capacity. Field test each anchor and certify each test by recording the date of the test, the force applied, and the person completing the test. Tabulate this data and deliver to the Engineer within 24 hours of completing the tests.

METHOD OF MEASUREMENT

650-4.1 By each set, consisting of 3 anchors, completed and accepted in final position.

BASIS OF PAYMENT

650-5.1 At the contract price, per set, for each of the pay items shown in the bid schedule.

Payment will be made under:

Item P650.020.0000	Soil Anchor Tie-down – per set

Item P650.030.0000	Rock Anchor Tie-down – per set

Item P650.040.0000	Temporary Tie-down – per each