## ITEM P-655	AIRCRAFT RELOCATION

DESCRIPTION

655-1.1 Move parked aircraft from the work area to a temporary parking area while work is in progress. Move the aircraft back to the parking apron following construction. Notify aircraft owners before moving aircraft to give them the opportunity to relocate their aircraft. If there is no response, accomplish the relocation.

REQUIREMENTS

655-2.1 NOTIFICATION. Notify the Engineer and Airport Manager a minimum of 14 calendar days prior to the requirement to remove aircraft from the area of apron to be reconstructed. You will be provided with each aircraft owners name, most current address, and telephone number. Make a minimum of three attempts on different days beginning a minimum of 10 days prior to the planned apron reconstruction start date. Document by phone log or other approved method your attempts to contact the owner. Repeat this process when work in an area is complete and ready to be reoccupied by aircraft.

Allow a minimum of 7 calendar days for aircraft owners to relocate their aircraft.

At the direction of the Engineer, relocate any aircraft that remain following the 7 day period allowed for owners to move their aircraft.

655-2.2 QUALIFIED PERSONNEL. Accomplish relocation of aircraft under the direct supervision of an aircraft maintenance technician in possession of a current A&P or AI license issued by the FAA.

655-2.3 TIE-DOWN MATERIAL. Tie aircraft down either in the temporary tie-down area or in a vacant tie-down space as directed by the Engineer. Secure each aircraft at 3 points; at each wing and the tail using 3 lengths of suitable 1/2-inch nylon rope. Tie-down rope used to tie down the aircraft at its original position may be used if, in the aircraft technician’s opinion, it is suitable for the purpose. If the existing tie-down ropes are not used, return these ropes to the owner and tie aircraft down with the new rope.

METHOD OF MEASUREMENT

655-4.1 For each aircraft relocated measured one way from permanently assigned tie-down to temporary tie-down or from temporary tie-down to permanently assigned tie-down.

BASIS OF PAYMENT

655-5.1 Payment for Aircraft Relocation will be full compensation for moving the aircraft to or from the temporary parking area including new tie-down ropes and for all labor, material and equipment needed to complete the item.

Payment will be made under:

Item P655.010.0000	Aircraft Relocation – per each