## ITEM P-660	RETROREFLECTIVE MARKERS AND CONES

DESCRIPTION

660-1.1 Furnish and install airport retroreflective markers and traffic cones in accordance with the plans, the safety plan, and the specifications at the locations indicated on the plans or as directed by the Engineer. Assemble and install markers using all materials and incidentals necessary to place completed markers into operation to the satisfaction of the Engineer. Remove existing reflective marker cones and threshold markers for salvage and offer to the owner for possession.

MATERIALS

660-2.1 MARKERS.

a.	Type l Marker. Semi-flush centerline marker conforming to FAA AC 150/5345-39, “Specification for L-853. Runway and Taxiway Lighting Retroreflective Markers” and certified under AC 150/5345-53 Airport Lighting Equipment Certification Program.

- Type II Marker. Elevated marker for edge marking conforming to FAA AC 150/5345-39, “Specification for L-853. Runway and Taxiway Lighting Retroreflective Markers” and certified under AC 150/5345-53 Airport Lighting Equipment Certification Program. Provide flexible or frangible markers in accordance with the height, marker colors, and retro-reflective colors shown on the plans. If not called on the plans, provide a finished marker height that is 30 inches above finish grade, marker color orange, and retroreflective colors as required by AC 150/5345-39. If frangible markers are supplied, ensure that the mounting system and tether are certified. When retro-reflective sheeting is used, provide manufacturer applied sheeting.

- Cone, 18-Inch. Reflective traffic cone, 18 inches in height, orange color. Fit each cone with retro-reflective sheeting to the height specified on the plans.  When no height dimension is specified, fit with a 7-inch wide band of retro-reflective sheeting centered on the cone. Use pressure sensitive, flexible, high intensity retroreflective sheeting, conforming to ASTM D4956, Type III. Provide the appropriate sheeting color(s) as indicated on the plans or if none is indicated supply with white colored band. Provide each cone with an anchoring tether of weather and corrosion resistant material capable of securing the assembly to prevent foreign object debris (FOD) hazard to aircraft similar to the tether required for Type II Markers that are frangible.

CONSTRUCTION REQUIREMENTS

660-3.1 Install markers and/or cones at the locations shown on the plans, called for in the specifications or as directed by the Engineer. Stabilize Type II Markers by using the manufacturer’s recommended methods of driving the supporting posts into the ground or providing a certified mounting system. If frangible Type II Markers or cones are provided, secure the tether to a hard point in accordance with AC 150/5345-39 per the manufacturer’s recommendations.

Remove existing reflective markers and threshold marking panels as shown on the plans or as directed for salvage and offer to the owner for possession. Markers not claimed by the owner become the property of the Contractor to be disposed of in a manner approved by the Engineer.

METHOD OF MEASUREMENT

660-4.1 The method of measurement will be by the number of markers or cones furnished and installed of the specified type, at locations approved by the Engineer.

Removal and salvaging of existing markers and panels will be subsidiary to the installation of reflective markers and/or cones and will not be measured for payment.

BASIS OF PAYMENT

660-5.1 Payment will be made at the contract unit price for each furnished and accepted item. This price will be full compensation for furnishing all materials, for all preparation, assembly, and installation of these materials, and for all labor, equipment, tools, and incidentals necessary to complete this item.

Payment will be made under:

Item P660.___.____	Reflective Marker, Type ____ – per each

Item P660.070.0000	Cone, 18 inch – per each