## ITEM P-670	HAZARDOUS AREA BARRIERS

DESCRIPTION

670-1.1 Provide barriers for use on the project under subsection 70-09, Barricades, Warning Signs and Hazard Markings. Provide each barrier complete with flasher unit and flag in accordance with the dimensions, design, and details shown on the Plans. Haul and place barriers as shown on the Plans or as directed by the Engineer. Relocate barriers as conditions warrant.

When used during periods of darkness, such barricades, warning signs and hazard markings shall be suitably illuminated. Barricades shall be spaced not more than 25 feet apart.

Provide additional flasher units and flags, when specified, for use on Department-supplied barriers.

MATERIALS

670-2.1 Use materials that conform to the following:

- Hazard Marker Barrier, Timber. Provide construction-grade Douglas Fir-Larch with nominal dimensions of 12 inches by 12 inches and a length of 8 feet. All timber that is exposed to weather, water, or soil shall be pressure treated to the current edition of the AWPA Standards, or AASHTO M 133, using preservatives registered with the US Environmental Protection Agency.  Products shall be treated according AWPA Standard U1, Use Category System. Use either oil base or latex exterior paint in colors international orange and white.

- Hazard Marker Barrier, Plastic. Provide 10-inch by 10-inch by 8-foot nominal dimension portable water-ballast barriers made from high impact, safety orange and white, UV-resistant, high density polyethylene (HDPE) plastic. Provide barriers with pre-molded flag staff and flasher bracket attachment holes. Provide barriers that are designed as a modular system to allow assembly/disassembly and nesting for compact storage, and to permit the option of physically bolting multiple barriers together to provide a continuous barrier wall. Provide 6-inch by 72-inch reflective striping panel for attachment to one side of each barrier.

670-2.2 Flag. Provide heavy vinyl coated nylon, 18-inch by 18-inch flag with an integral diagonal metal or plastic stay to make the flag self-supporting. Provide flag in color fluorescent orange and mounted on a 3/4-inch by 30-inch staff.

670-2.3 Flasher Unit. Provide battery-operated omnidirectional flashing red light. Provide flasher unit with mounting bracket designed for the appropriate barrier type.

- Flasher Unit for Timber Barrier. Meet Manual on Uniform Traffic Control Devices (MUTCD) requirements for Type A Warning Lights. Supply one set of non-standard tools, such as the on/off switch or battery access tool, for each 5 flasher units furnished.

- Flasher Unit for Plastic Barrier.

| Composition | High impact, polycarbonate plastic lens and base |
| --- | --- |
| Flashing Rate | 60 flashes per minute |
| Brightness | 6000 mcd |
| LED | Total of 3 red |
| Photo Cell | Allows for solar light to automatically shut off in higher level light conditions and turn on in lower light conditions |

CONSTRUCTION REQUIREMENTS

670-3.1 GENERAL. On the top side and at opposite ends of each barrier, mount one flag and one flasher unit per manufacturer’s instructions. Tether flag to the barrier.

- Hazard Marker Barrier, Timber.

  - Preparation. Prior to painting, notch the underside of each timber to allow for the use of a forklift. Cut two 4-inch high by 12-inch wide notches spaced 36 inches center to center, centered on the long axis of the timber.

  - Painting. Apply one coat of primer and one coat of finish white color paint on all sides and the ends followed by two coats of orange finish paint to form the stripes on the sides. Paint orange stripes 24 inches wide and offset by 6 inches from one side to the next giving a “barber pole” effect.

  - Flag and Flasher Unit. Mount the flag 24 inches from one end of the timber by drilling a hole 1/8-inch larger than the diameter of the staff by 8 inches deep. Mount the flasher unit 24 inches from the opposite end of the timber.

b.	Hazard Marker Barrier, Plastic. Fill barriers with water for ballast in accordance with manufacturer’s recommendations. When shown on the plans or directed by the Engineer, interlock barrier units using manufacturer recommended connectors to form a continuous wall separating the hazardous work area from aircraft movement areas. Adhere reflective striping panels to one side of each barrier.

670-3.2 DELIVERY. Deliver hazard marker barriers, flasher units, and flags to the project site prior to commencing work within the Air Operations Area.

METHOD OF MEASUREMENT

670-4.1 Hazard marker barriers, complete with flag and flasher unit will be measured by the number of units furnished and accepted.

Flasher units and flags to be used on Department-supplied barriers will be measured by the number of units furnished and accepted.

BASIS OF PAYMENT

670-5.1 Payment covers all costs associated with furnishing and storing hazard marker barriers, flasher units, and flags, including tools, batteries, and incidentals.

Work required for placing, erecting, moving, and maintaining barriers is subsidiary.

Payment will be made under:

Item P670.___.____	Hazard Marker Barrier, Plastic – per each

Item P670.___.____	Flasher Unit for ____ Barrier – per each

Item P670.050.0000	Flag – per each