## ITEM T-901	SEEDING

DESCRIPTION

901-1.1 This work consists of preparing the ground and applying seed and fertilizer in conformance with the Plans and Specifications.

The intent of this work is to provide a living vegetative cover in the areas indicated on the Plans and to maintain the cover for the term of the Contract.

MATERIALS

901-2.1 SEED. Provide the seed mixture as specified in the Special Provisions. Provide seed collected or harvested within 2 years of the targeted seeding date. Provide all seed in pure live seed (PLS) unless otherwise directed.

Provide seed true of genus and species.  Meet the applicable requirements of the State of Alaska Seed Regulations, 11 AAC 34, Articles 1 and 4, and the Federal Seed Act, 7 CFR Part 201.

The Engineer will review requests for species or cultivar substitution(s); genus substitution is not allowed. Substitution requests need to be submitted a minimum of 60 calendar days in advance of delivery.

- Prohibited and Restricted Noxious Weeds and Quarantined Pests.  Provide seed and appliances certified to be free of prohibited noxious weeds or quarantined pests, and certified to contain no more than the maximum allowable tolerances for restricted noxious weeds, according to Alaska Administrative Code, Title 11, Chapter 34 (11 AAC 34).

  - Seed or appliances found to contain prohibited noxious weeds or quarantined pests will be rejected, according to 11 AAC 34.020(a) and 11 AAC 105-180, respectively.

  - Seed or appliances found to contain restricted noxious weed seed in excess of the maximum allowable tolerance per pound will be rejected, according to 11 AAC 34.020(b).

  - Prohibited and restricted noxious weeds are listed in 11 AAC 34.020, and can be viewed at the following URL: http://plants.alaska.gov/invasives/noxious-weeds.htm.

- Labeling. Ensure each bag or container of individual seed species is labeled to meet requirements of 11 AAC 34.010. Do not remove labels from bags or containers.

- Certification.  Certify seed is free of prohibited noxious weeds and restricted noxious weeds are within allowable tolerances.  Provide to the Engineer no later than 10 days prior to seeding 4 signed copies of a statement signed by the vendor identifying the lot number or lot numbers, certifying each lot of seed has been tested within the preceding nine months, by a recognized seed testing laboratory, a member of the Association of Official Seed Certifying Agency (AOSCA), or the Alaska Plant Materials Center.

Include the following in each certification:

  - name and address of laboratory

  - date of test

  - lot number

  - seed name

  - percent pure seed

  - percent germination

  - percent weed content

  - percent inert matter

Seed will be rejected if:

- Contains prohibited noxious weeds;

- Contains restricted noxious weeds above maximum allowable tolerances;

- Not certified as tested within the preceding nine months;

- Wet, moldy, or otherwise damaged in transit or storage; or

- Containers do not have labels or the labels have been removed.

Seed may be rejected for:

- Discrepancies in the lot numbers listed on the statement to the lot numbers indicated on the labels of the seed containers.

The Contractor shall immediately remove rejected seed from the project premises.  If seed is rejected for containing prohibited noxious weeds or for exceeding maximum allowable tolerances of restricted noxious weeds, dispose of rejected seed according to 11 AAC 34.075(g).

    - FERTILIZER. Provide a 20-20-10 fertilizer containing no cyanamid compounds or hydrated lime. Tolerances of the chemical ingredients shall be plus or minus 2%.

Use standard commercial fertilizer supplied separately or in mixtures, and in moisture proof containers. Mark each container with the total net weight and with the manufacturer’s guaranteed analysis of the contents showing the percentage for each ingredient.

CONSTRUCTION METHODS

901-3.1 SOIL PREPARATION. Clear all areas to be seeded of stones 4 inches in diameter and larger and of all sticks, stumps, noxious weeds, and other debris or irregularities that might interfere with the seeding operation, growth of grass, or subsequent maintenance of the grass covered areas.

Just prior to seeding, roughen the surface of all areas to be seeded by track-walking transversely up and down the slopes or using a scarifying slope board. Round the top and bottom of the slopes, when necessary, to facilitate tracking and to create a pleasing appearance, but do not disrupt drainage flow lines. Where fill is adjacent to wetlands, keep the equipment entirely on the fill slope.

901-3.2 SEEDING SEASONS. Seed and fertilize between May 15 and August 15.

Do not seed during windy conditions or when climatic conditions or ground conditions would hinder placement or proper growth.

901-3.3 APPLICATION. Apply seed and fertilizer at the rates specified in the Special Provisions. Use either of the following methods:

- Hydraulic Method.

  - Mix a slurry of seed, fertilizer, water, and other components as required by the Special Provisions. Add seed to the slurry mixture no more than 30 minutes before application.

  - Use hydraulic seeding equipment that will maintain a continuous agitation and apply a homogeneous mixture through a spray nozzle. The pump must produce enough pressure to maintain a continuous nonfluctuating spray that will reach the extremities of the seeding area, without causing damage to the seed bed. Use a hose attachment to reach areas where a fixed nozzle cannot reach.

  - If mulch material is required, add it to the water slurry in the hydraulic seeder after adding the proportionate amounts of seed and fertilizer.

  - Apply slurry at a rate that distributes all materials evenly.

- Dry Method.

  - Use mechanical spreaders, seed drills, landscape seeders, cultipacker seeders, fertilizer spreaders, or other approved mechanical spreading equipment.

  - Moisten the soil prior to the application of seed and fertilizer and immediately afterwards.

  - Mix or rake the seed and fertilizer into the seed bed to a depth of 1/2 inch, unless mulch material is to be applied immediately.

901-3.4 MAINTENANCE OF SEEDED AREAS. Protect seeded areas against traffic using approved warning  signs or barricades. Repair surfaces that are gullied or otherwise damaged following seeding by regrading and reseeding, as directed. Maintain seeded areas in a satisfactory condition until final inspection and acceptance of the work.

Keep temporary erosion control measures in place until the vegetation is accepted.

Water the seeded areas, as required, for proper germination and growth. Use equipment that can acceptably water all seeded areas without vehicular traffic on seeded areas.

Reseed any seeded areas not showing evidence of satisfactory growth, as directed.

901-3.5 FINAL ACCEPTANCE. Final acceptance will be based on the following criteria and must provide 70% vegetative coverage of the seeded area. If seeding is completed by July 15th, coverage must be attained by September 30th. If seeding is completed by August 15th, coverage must be attained by June 15th of the following season. Final acceptance will be based on the Engineers approval.

METHOD OF MEASUREMENT

901-4.1 The work will be measured according to Subsection 90-02, and as follows:

- Seeding by the acre. By the area of ground surface acceptably seeded, fertilized, and maintained. Required reseeding is subsidiary.

- Seeding by the pound. By the weight of seed acceptably placed. Fertilizer is subsidiary. Any other work required will be measured separately.

- Water for maintenance. By the M-gal (1,000 gallons) acceptably placed. Use a conversion factor of 8.34 pounds per gallon, if measured by weight. Use a conversion factor of 7.48 gallons per cubic foot, if measured by volume.

BASIS OF PAYMENT

901-5.1 Soil preparation, fertilizer, and water required for hydraulic method are subsidiary. Mulching will be measured and paid for under Item T-908.

- Seeding by the Acre. Payment is for established vegetative mat.

- Seeding by the Pound. Payment is for established vegetative mat.

- Water for Seeding. Water applied for growth of vegetative mat.

Payment will be made under:

Item T901.010.0000	Seeding – per acre

Item T901.020.0000	Seeding – per pound

Item T901.030.0000	Water for Maintenance – per Mgal