## ITEM T-903	SPRIGGING

DESCRIPTION

903-1.1 This item shall consist of planting sprigs of living grass plants at the locations shown on the plans or as directed by the Engineer in accordance with these Specifications.

MATERIALS

903-2.1 SPRIGS. Sprigs shall be healthy living stems (stolons or rhizomes), of native beach wildrye (Leymus mollis), harvested from areas within the airport property as shown on the plans or as directed by the Engineer. The presence of weeds or other material which might be detrimental to the proposed planting will be cause for rejection of sprigs.

903-2.2 NOT USED.

903-2.3 FERTILIZER. Provide a 20-20-10 fertilizer containing no Cyanamid compounds or hydrated lime. Tolerances of the chemical ingredients shall be plus or minus 2%.

Use standard commercial fertilizer supplied separately or in mixtures, and in moisture proof containers. Mark each container with the total net weight and with the manufacturer’s guaranteed analysis of the contents showing the percentage for each ingredient.

903-2.4 WATER. All water used shall be sufficiently free from oil, acid, alkali, salt, or other harmful materials that would inhibit the growth of grass. Brackish water shall not be used at any time. It shall be subject to the approval of the Engineer prior to use.

CONSTRUCTION METHODS

903-3.1 GENERAL. Sprigging shall be done in accordance with the recommendations contained in the booklet, “Beach Wildrye Planting Guide for Alaska”, 1994 by Stoney Wright with the Alaska Plant Materials Center located in Palmer, Ph. (907) 745-4469.  This booklet can be downloaded at: http://plants.alaska.gov/reveg/coastal_06_beach-wildrye.php.

903-3.2 ADVANCE PREPARATION AND CLEANUP. After grading of areas has been completed and before applying fertilizer, areas to be sprigged shall be raked or otherwise cleared of stones larger than 2 inches in any diameter, sticks, stumps, and other debris which might interfere with sprigging, growth of grasses, or subsequent maintenance of grass-covered areas. If any damage by erosion or other causes has occurred after grading of areas and before beginning the application of fertilizer, the Contractor shall repair such damage. This may include filling gullies, smoothing irregularities, and repairing other incidental damage.

903-3.3 APPLYING FERTILIZER. Following advance preparation and cleanup, fertilizer shall be uniformly spread at a rate which will provide not less than the minimum quantity of each fertilizer ingredient as stated in the special provisions. Apply fertilizer at the rate of 550 pounds per acre. Apply fertilizer with power sprayers, blower equipment, or other approved methods.

903-3.4 HARVESTING SPRIGS. Harvesting may be performed by any method acceptable to the Engineer, including crisscross cultivation, shallow plowing, or other acceptable methods to thoroughly loosen the sprigs from the soil and to bring them to the surface. After loosening the sprigs from the soil, they shall be gathered in small piles or windrows, watered, and kept moist until planted. Stockpile sprigs in designated or approved areas.

Sprigs that have heated in stockpiles, have become frozen, permitted to dry out, or otherwise seriously damaged during harvesting or delivery shall be rejected and shall be disposed of as directed by the Engineer.

903-3.5 PLANTING SPRIGS. Accomplish planting and fertilizing after June 1 and before September 1. Sprigging shall not be done during windy weather, or when the ground is dry, excessively wet, frozen, or otherwise untillable. If the soil is not moist when the sprigs are being set, water shall be applied until the soil is moist and in a workable condition.

Furrows shall be opened along the approximate contour of slopes at 3 foot spacings and 5 inches in depth. Sprigs shall be placed without delay in the open furrow at 3 foot on center spacing, and the roots of each sprig shall be covered immediately with soil by employing the “drop and stomp” planting method. Provide sprig spacing uniformity of plus-minus 6 inches. Provide depth uniformity of plus-minus 1 inch.

903-3.6 Not used.

903-3.7 ESTABLISHING TURF. The Contractor shall be responsible for the proper care of the sprigged areas during the period when the plants are becoming established and he shall protect the sprigged areas against traffic by warning signs or barricades approved by the Engineer. Surfaces gullied or otherwise damaged following sprigging shall be repaired by regrading and resprigging as directed. The Contractor shall water as directed, and otherwise maintain sprigged areas in a satisfactory condition until final inspection and acceptance of the work.

METHOD OF MEASUREMENT

903-4.1 Sprigging shall be measured by area, measured on the ground surface, completed and accepted.

BASIS OF PAYMENT

903-5.1 Payment will be made at the contract unit price. This price shall be full compensation for providing and placing all material including fertilizing and watering of sprigged areas, and for all labor, equipment, tools, and incidentals necessary to complete the work prescribed in this item.

Payment will be made under:

Item T903.010.0000	Sprigging – per acre

Item T903.020.0000	Sprigging – per square yard