## ITEM T-920	VEGETATIVE MAT

DESCRIPTION

920-1.1 Establish living vegetative cover by transplanting vegetative mats at the locations shown on the plans or as directed by the Engineer. Maintain the transplanted vegetative cover for the term of the contract.

MATERIALS

920-2.1 VEGETATIVE MAT. Use the vegetative mat from the portion of the existing slough impacted by construction.

920-2.2 FERTILIZER. If needed, use fertilizer that conforms to the requirements of 901-2.2 Fertilizer, using the same application rate specified in 901-3.3 Application. Fertilizers should generally not be necessary for transplanting vegetative mats, but may be required for soil repairs in 920-2.4.

920-2.3 WATER. Ensure that the water is sufficiently free from oil, acid, alkali, salt, or other harmful materials that would inhibit the growth of grass.

920-2.4 SOIL FOR REPAIRS. Use native soils similar to those found at the source of the relocated vegetative mats for fill of areas to be repaired.

CONSTRUCTION METHODS

920-3.1 GENERAL. Prepare the areas to be revegetated with mats by removing rocks larger than 2 inches in any diameter, logs, wood, and other debris. Dispose of debris below grade in areas to be restored or in other approved disposal areas. Grade subsoil so top surface of relocated vegetative mat will be at finish grade.

920-3.2 OBTAINING AND STORING VEGETATIVE MAT. Remove the vegetative mat from the slough or designated source using a backhoe and measure in size according to the size of the backhoe bucket. Dig a test hole to determine the depth of the vegetative mat which will be the depth where most of the roots/rhizome matter is retained. Stockpile the vegetative mat on heavy-duty impervious construction plastic. Staple the sides of the plastic together to create a wall effect to trap moisture. Keep the vegetative mat moist. Do not cover the vegetative mat during stockpiling, except when it is transported (rolling the plastic will facilitate the transportation of the vegetative mat in one piece; in case the vegetative mat breaks apart, then the individual broken pieces can be independently planted). Stockpile the vegetative mat for a minimal amount of time within the construction area for up to six months, or as directed by the Engineer.

920-3.3 LAYING VEGETATIVE MAT. Scarify or add soil as necessary to the plant site to promote root growth, then add vegetative mat. Tap down the mat so that it is in direct contact with the soil, and water the mat thoroughly.

920-3.4 WATERING. Ensure that adequate water and watering equipment is on hand before relocating vegetative mat. Keep vegetative mat moist until it has become established and continued growth is assured. Water in a manner that will avoid erosion from the application of excessive quantities and avoid damage to the finished surface.

920-3.5 REPAIRING. When the surface has become bullied or otherwise damaged during the period covered by this contract, repair the affected areas to re-establish the grade and the condition of the soil, as directed by the Engineer.

METHOD OF MEASUREMENT

920-4.1 GCP Section 90 by the unit area of surface covered with vegetative mat in final position as accepted by the Engineer.

BASIS OF PAYMENT

920-5.1 This item will be paid for on the basis of the contract unit price per square yard for relocated vegetative mat in final position as full compensation for all labor, equipment, material, staking, and incidentals necessary to satisfactorily complete the items as specified. Water for maintenance is subsidiary except when it is listed in the bid schedule.

Payment will be made under:

Item T920.010.0000	Relocate Vegetative Mat – per square yard

Item T920.020.0000	Water for Maintenance – per Mgal